## Slide 1
B25 FIT — LEVEL 01 PROJECT
Autonomous Ring Toss Launcher Robot
An IoT-Enabled, Vision-Guided Precision Launching System
Degree Programme
BSc (Hons) in Information Technology / Information Technology & Management
Supervised By
[Supervisor Name]
Project Team
254037B
CHAMIDYA J.A.S
(IT)
254048J
DE SILVA P.S.S
(IT)
255078H
OMESH N.A.N
(ITM)
254101R
KALANSOORIYA O.K
(IT)
255027D
GOONATILLAKA W.A.D.S.S
(ITM)

## Slide 2
Introduction
Ring toss is a classic precision game that traditionally depends on human aim and consistency. This project introduces an autonomous ring-toss launcher robot that fuses mechanical design, embedded control, and computer vision to consistently and safely land rings on a target peg.
The system integrates a dual-flywheel launching mechanism, a motorised pan-tilt aiming base, and a companion computer running real-time object detection, all coordinated through a low-level microcontroller. A mobile dashboard enables both fully autonomous operation and manual override, making the platform suitable for demonstration, competition, and further research into robotic targeting.
3
Integrated Subsystems
Mechanical · Electronic · AI
5
Team Members
Cross-functional roles
10
Month Development Timeline
Design to demonstration
2

## Slide 3
Aim & Objectives
AIM
To design, build, and demonstrate an autonomous ring-toss launcher robot capable of detecting a target peg, calculating the required trajectory, and consistently landing rings on the target with minimal human intervention.
OBJECTIVES
01
Design a reliable dual-flywheel launching mechanism with a controlled ring-feeding system.
02
Develop a 2-axis pan-tilt aiming platform driven by high-torque stepper motors.
03
Implement real-time computer vision to detect the target and estimate distance.
04
Build low-level firmware with closed-loop PID control for flywheel RPM and aiming accuracy.
05
Integrate a safety interlock system to prevent accidental injury during operation.
06
Create a mobile/web dashboard for manual control, telemetry, and mode switching.
3

## Slide 4
Problem & Proposed Solution
THE PROBLEM
—
Manual ring-toss aiming is inconsistent and heavily skill-dependent.
—
Existing toy launchers lack sensing, feedback, or safety mechanisms.
—
No affordable platform combines precision mechanics with autonomous targeting for educational demonstration.
—
Repeated manual tuning is required whenever distance or environment changes.
PROPOSED SOLUTION
—
An IoT-enabled robot that autonomously detects the target using computer vision and LiDAR.
—
Closed-loop control ensures consistent flywheel speed and aiming angle for every shot.
—
A built-in safety tripwire disables the launcher automatically if a person enters the firing path.
—
Dual-mode operation (autonomous + manual) via a companion app, with live telemetry.
4

## Slide 5
System Block Diagram
Solid line = data / control signal Dashed line = power supply
Mobile / Web Dashboard
Manual control + live telemetry
Raspberry Pi 5
Computer Vision & AI Targeting
ESP32 Microcontroller
Real-Time Control · PID · Motion
Power Distribution PCB
Fuse + E-Stop + Voltage Regulators
LiPo Battery Pack
Main Power Source
UART / SPI
Camera Module 3
12MP — visual target detection
TF-Luna LiDAR
Distance to target (0.2–8 m)
IR Break-Beam Sensor
Confirms ring exit / feed
Motor Encoders
Flywheel RPM feedback
Ultrasonic Tripwire
Safety interlock sensor
Flywheel Launch Motors (×2)
Brushless DC + 30A ESC
Pan-Tilt Gimbal
2× NEMA17 Stepper + Driver
Ring Feeder Servo
MG996R — feeds one ring per shot
Data / control signal
Power supply line
5

## Slide 6
Operational Flow
From power-on to power-off — one complete firing cycle
1
Power ON
Battery engaged; PDB initialises regulated rails; ESP32 and Pi 5 boot.
2
Self-Check
Firmware runs sensor & motor diagnostics; safety tripwire armed.
3
Mode Select
Operator chooses Autonomous or Manual mode on the dashboard.
4
Target Acquisition
Camera + LiDAR locate the peg (Auto) or operator aims manually.
5
Trajectory Calc.
ESP32 computes required flywheel RPM and tilt angle.
6
Aim
Pan-tilt gimbal rotates to the calculated bearing and elevation.
7
Spin-Up
Flywheel motors reach target RPM, confirmed by encoder feedback.
8
Feed & Fire
Feeder servo pushes a ring in; IR sensor confirms ring exit.
9
Telemetry Update
Shot count, RPM and battery level sent to the dashboard.
10
Repeat / Power OFF
Loop to Step 3 for the next shot, or shut down safely.
Example: Target detected at 2.4 m → tilt angle 18° → flywheel speed 3,200 RPM → ring launched → lands within 10 cm of the peg.
6

## Slide 7
Hand-Drawn System Sketch
Concept sketch — to be inserted
Paste your hand-drawn sketch here
7

## Slide 8
Hardware Components
Complete bill of hardware used in the system
Component | Specification | Qty | Function
Raspberry Pi 5 (8GB) | Companion computer | 1 | Runs computer vision & AI targeting
ESP32 Dev Board | Dual-core MCU | 1 | Real-time motor & sensor control
Raspberry Pi Camera Module 3 | 12MP, autofocus | 1 | Visual target detection
TF-Luna LiDAR | Single-point ToF, 0.2–8 m | 1 | Distance measurement to target
Brushless Outrunner Motor | 2200KV | 2 | Flywheel ring launching
Electronic Speed Controller (ESC) | 30A | 2 | Drives flywheel motors
NEMA 17 Stepper Motor | 1.5A, 42mm | 2 | Pan & tilt aiming
Stepper Driver (A4988 / TMC2209) | Micro-stepping | 2 | Stepper motor control
MG996R Servo Motor | 180°, 10kg·cm | 1 | Ring feeding mechanism
IR Break-Beam Sensor | Digital output | 1 | Confirms ring exit
Motor Encoder | Magnetic / optical | 2 | Flywheel RPM feedback
Ultrasonic Sensor (HC-SR04) | 2–400 cm range | 1 | Safety tripwire interlock
LiPo Battery | 4S, ≥5000mAh | 1 | Main power source
Power Distribution PCB | Custom design | 1 | Voltage regulation & protection
Fuse & Emergency Stop Switch | Inline, rated | 1 set | Overcurrent & emergency safety
3D-Printed Chassis Parts | PLA / PETG | — | Structural housing
Acrylic / Aluminium Frame Plates | 3mm | — | Structural support
8

## Slide 9
Software Components & Technologies
Firmware
• C / C++
• Arduino / ESP-IDF framework
• Closed-loop PID control library
Computer Vision & AI
• Python
• OpenCV
• YOLOv8-Nano (Ultralytics)
• NumPy
Companion Computer OS
• Raspberry Pi OS (64-bit)
Communication
• UART · SPI
• Wi-Fi · Bluetooth Low Energy
• WebSocket / MQTT telemetry
Mobile / Web Dashboard
• React or Flutter
• Real-time WebSocket telemetry
Design & Simulation
• SolidWorks / Fusion 360 (CAD)
• Python — ballistics modelling
9

## Slide 10
Power System
How the robot is powered — from battery to every subsystem
A high-discharge LiPo pack supplies the surge current needed by the flywheel motors at launch.
The Power Distribution PCB regulates and isolates rails: 5V logic, 3.3V sensors, and raw voltage for motor drivers.
An inline fuse and emergency-stop switch provide overcurrent and manual safety protection.
A voltage/current sensor feeds live battery telemetry to the dashboard for continuous monitoring.
LiPo Battery Pack
Fuse + Emergency Stop
Power Distribution PCB
5V Regulated Rail
Raspberry Pi 5, logic ICs
3.3V Regulated Rail
ESP32, IR / LiDAR / ultrasonic sensors
Raw Battery Rail (via ESC)
Flywheel motors, steppers, feeder servo
10

## Slide 11
Project Budget
Estimated cost in LKR
Category | Item | Qty | Unit Cost (LKR) | Total (LKR)
Mechanical | 3D-printed parts & filament | — | 15,000 | 15,000
Mechanical | Acrylic / aluminium plates | — | 8,000 | 8,000
Mechanical | Fasteners & hardware | — | 3,000 | 3,000
Electronics | Raspberry Pi 5 (8GB) | 1 | 45,000 | 45,000
Electronics | ESP32 dev board (incl. spare) | 2 | 1,500 | 3,000
Electronics | Brushless motor 2200KV | 2 | 4,500 | 9,000
Electronics | ESC 30A | 2 | 3,000 | 6,000
Electronics | NEMA17 stepper motor | 2 | 3,500 | 7,000
Electronics | Stepper driver (TMC2209) | 2 | 1,250 | 2,500
Electronics | MG996R servo | 1 | 1,800 | 1,800
Sensors | Camera Module 3 | 1 | 9,500 | 9,500
Sensors | TF-Luna LiDAR | 1 | 7,000 | 7,000
Sensors | IR break-beam sensor | 1 | 500 | 500
Sensors | Motor encoders | 2 | 1,500 | 3,000
Sensors | Ultrasonic sensor (HC-SR04) | 1 | 400 | 400
Power | LiPo battery 4S 5000mAh | 1 | 9,000 | 9,000
Power | Power distribution PCB (fab.) | 1 | 4,000 | 4,000
Power | Fuse + E-stop switch | 1 | 1,500 | 1,500
Power | Wiring & connectors | — | 2,000 | 2,000
Software / Misc. | Testing consumables & misc. | — | 5,000 | 5,000
Subtotal 142,200 + Contingency (10%) 14,220 = 156,420 LKR
11

## Slide 12
Project Timeline
10-month development plan
M1
M2
M3
M4
M5
M6
M7
M8
M9
M10
Requirement Analysis & Research
Mechanical Design (CAD) & Ballistics Calc.
Electronics & PCB Design
Mechanical Fabrication & Assembly
Firmware Development (Motor / PID / Feeder)
Computer Vision & AI Model Training
Pan-Tilt & Targeting Integration
Mobile / Web Dashboard Development
System Integration & Safety Testing
Field Testing & Calibration
Documentation & Final Report
Final Demonstration & Viva
12

## Slide 13
Work Distribution
Each member owns at least one sensor and one hardware module
Member | Programme | Primary Role | Assigned Sensor(s) | Assigned Hardware Module(s)
Chamidya J.A.S | IT | Mechanical Lead | IR Ring-Exit Sensor | Flywheel housing & feeder mechanism (chassis)
De Silva P.S.S | IT | Electrical / Power Lead | Voltage & current monitor | Power distribution PCB, battery, fuse / E-stop
Omesh N.A.N | ITM | Embedded Firmware Lead | Motor encoders (RPM feedback) | ESP32 control board, ESC & motor driver wiring
Kalansooriya O.K | IT | Computer Vision Lead | Camera Module 3, TF-Luna LiDAR | Raspberry Pi 5 unit, pan-tilt gimbal assembly
Goonatillaka W.A.D.S.S | ITM | Systems / UI Lead | Ultrasonic safety tripwire | Mobile / web dashboard, telemetry module
13

## Slide 14
Why This System Stands Out
Autonomous Targeting
Onboard computer vision + LiDAR depth sensing locate the target without human aim.
Consistent Accuracy
Closed-loop PID control guarantees repeatable shots — not open-loop like typical toys.
Built-In Safety
A tripwire interlock automatically disables launch power if the firing path is obstructed.
Dual-Mode Operation
Seamless switching between autonomous AI targeting and manual joystick control.
Live Telemetry
Real-time dashboard tracks battery level, flywheel RPM, and shot count.
Modular IoT Architecture
New sensors, ML models, or targets can be added without redesigning the system.
14

## Slide 15
References
[1]
Bradski, G. (2000). The OpenCV Library. Dr. Dobb's Journal of Software Tools.
[2]
Jocher, G., Chaurasia, A., & Qiu, J. (2023). Ultralytics YOLOv8. GitHub repository. https://github.com/ultralytics/ultralytics
[3]
Raspberry Pi Foundation. (2024). Raspberry Pi 5 Documentation. https://www.raspberrypi.com/documentation/
[4]
Espressif Systems. (2023). ESP32 Series Technical Reference Manual. https://www.espressif.com/
[5]
Ogata, K. (2010). Modern Control Engineering (5th ed.). Prentice Hall.
[6]
Texas Instruments. (2022). Brushless DC Motor Fundamentals. Application Note.
[7]
Trinamic / Analog Devices. (2023). TMC2209 Datasheet — Stepper Motor Driver.
[8]
Benet-Sole (TF-Luna). (2022). TF-Luna LiDAR Module Product Manual.
15

## Slide 16
Thank You
Questions & Discussion
Autonomous Ring Toss Launcher Robot — B25 FIT Level 01 Project