## Slide 1
B25 FIT LEVEL 01 PROJECT
AquaScout
An IoT-Enabled Underwater Exploration Drone (ROV)
254037B
CHAMIDYA J.A.S
(IT)
254048J
DE SILVA P.S.S
(IT)
255078H
OMESH N.A.N
(ITM)
254101R
KALANSOORIYA O.K
(IT)
255027D
GOONATILLAKA W.A.D.S.S
(ITM)
Degree Programme: BSc (Hons) in Information Technology / Information Technology Management
Supervisor: [Supervisor Name]

## Slide 2
02
Introduction
Background and context for the proposed underwater drone system
Oceans, lakes, reservoirs, and industrial water tanks remain some of the least accessible environments for direct human inspection. Diving is costly, time-limited, and hazardous, while existing commercial ROVs (Remotely Operated Vehicles) are often too expensive for small-scale research, education, or local inspection needs.
This project proposes an affordable, tethered, IoT-enabled underwater drone capable of live video streaming, depth and orientation sensing, and remote piloting from a surface control station — built using accessible microcontrollers, sensors, and off-the-shelf components.
WHY THIS MATTERS
Radio signals do not propagate through water — a tethered link is required for reliable control and data transfer.
Underwater exploration supports marine research, pipeline/hull inspection, and search-and-recovery tasks.
A low-cost, modular drone makes underwater robotics accessible for academic and community use.
Combining embedded sensing (IoT) with real-time telemetry creates a safer, data-driven piloting experience.

## Slide 3
03
Aim & Objectives
What the project sets out to achieve
AIM
To design and develop a low-cost, tethered, IoT-enabled underwater drone that can be remotely piloted to capture live video and environmental telemetry while maintaining stable depth and orientation.
01
Design a waterproof, neutrally-buoyant hull and frame capable of withstanding shallow-water pressure.
02
Integrate propulsion (thrusters + ESCs) for controlled forward, lateral, and vertical movement.
03
Implement embedded sensing (IMU, depth, leak) with a PID-based stabilisation algorithm.
04
Establish a reliable wired (RS-485) communication link over a 20–50 m tether.
05
Build a surface control station with a joystick interface and live video/telemetry GUI.
06
Test, calibrate, and validate the complete system in a controlled water environment.

## Slide 4
04
Problem & Proposed Solution
The gap in accessible underwater inspection, and how we address it
THE PROBLEM
Human diving for inspection or exploration is expensive, physically risky, and time-restricted.
Radio-based (Wi-Fi/Bluetooth) drones fail underwater since radio waves do not propagate through water.
Commercial ROVs (e.g., Blue Robotics-class systems) are costly and inaccessible for small teams.
Manual piloting without sensor feedback makes it difficult to hold a stable depth or heading.
Existing budget builds often lack integrated safety features such as leak detection or fail-safes.
THE PROPOSED SOLUTION
A tethered underwater drone using a Cat5e/Cat6 + RS-485 link for reliable control at 20–50 m depth/range.
A modular, low-cost hardware build using an ESP32/Arduino Mega, DIY-viable thrusters, and 3D-printed parts.
Onboard IMU + depth sensor with a PID stabilisation loop for automatic depth/orientation hold.
A surface GUI with live video and telemetry (depth, heading, battery, leak status) for informed piloting.
Integrated leak detection and a positive-buoyancy fail-safe so the drone surfaces automatically on fault.

## Slide 5
05
System Architecture — Block Diagram
Every sensor, module, and signal/power path, from the submersible unit to the surface station
SUBMERSIBLE UNIT
LiPo Battery
(3S / 4S)
Power Distribution
Board (PDB)
Fuse & Kill Switch
Power Supply
IMU
(MPU6050)
Depth / Pressure
Sensor (MS5837)
Leak Detection
Sensor
Camera
(FPV / USB)
Microcontroller — ESP32 / Arduino Mega
(Central Processing Unit)
PROPULSION
4 x ESC (Electronic
Speed Controllers)
4 x Brushless Thrusters
(2 Horizontal + 2 Vertical)
RS-485 Transceiver
(MAX485)
PDB regulates and fuses power from the battery to every module; the kill switch cuts all power instantly.
TETHER
Cat5e/Cat6, 20–50 m
RS-485 Data + Power
SURFACE STATION
Joystick / Controller
Control Laptop
Live Video + Telemetry GUI
(depth, heading, battery, leak alerts)
RS-485 Transceiver
(MAX485)
The laptop GUI both sends pilot commands down the tether and receives live sensor/video telemetry back.
Control / Sensor Data Signal
Power Line
Bidirectional Tether Link

## Slide 6
06
Operational Flow
From power-on to power-off — how the system behaves during a dive
1
Power ON
Surface station and drone battery are activated; kill switch engaged.
2
System Initialisation
MCU boots and calibrates the IMU, depth sensor, and leak sensor.
3
Comms Handshake
RS-485 link is established between surface and drone over the tether.
4
Pilot Input
Operator moves the joystick on the surface control station.
5
Command Transmission
Movement commands travel down the tether to the onboard MCU.
6
Motor Actuation
MCU drives the ESCs via PWM; thrusters move the drone (fwd/lateral/vertical).
7
Stabilisation Loop
IMU + depth data feed a PID loop that auto-holds depth and orientation.
8
Live Feedback
Video and telemetry (depth, battery, leak) stream back to the surface GUI.
9
Safety Monitoring
Leak/battery faults trigger an automatic ascent to the surface.
10
Power OFF
Operator ends the session; kill switch cuts power and the drone floats up.
EXAMPLE SCENARIO — PIPELINE INSPECTION
The drone descends to 5 m and automatically holds that depth. The operator pans the camera to inspect a submerged pipeline, then commands ascent; the drone surfaces safely and power is switched off.

## Slide 7
07
Hand-Drawn Concept Sketch
Placeholder — original sketch to be inserted here
Insert hand-drawn concept sketch image here

## Slide 8
08
Why This System Stands Out
Design choices that differentiate this build from typical low-budget ROVs
Automatic Depth & Orientation Hold
IMU + pressure sensor feed a PID loop, so the pilot doesn't have to fight drift manually.
Reliable Long-Tether Communication
RS-485 over Cat5e/Cat6 stays stable at 20–50 m, where radio-based control would fail entirely.
Built-In Fail-Safes
Leak detection and a positive-buoyancy hull mean the drone surfaces on its own if something goes wrong.
Full Live Telemetry Overlay
Depth, heading, battery, and leak status are shown alongside the video feed for informed piloting.
Low-Cost, Modular Build
Accessible components (ESP32/Arduino, DIY-viable thrusters, 3D-printed brackets) keep cost far below commercial ROVs.
Serviceable by Design
A removable internal electronics sled lets the team reprogram or repair the drone without re-sealing the hull each time.

## Slide 9
09
Hardware Components
Complete parts list across the submersible unit and surface station
PROCESSING
ESP32 / Arduino Mega (main microcontroller)
MAX485 RS-485 transceiver modules (x2)
SENSING
MPU6050 IMU (orientation)
MS5837 depth / pressure sensor
Leak detection probe
FPV / USB camera module
PROPULSION
4x waterproof brushless thrusters (or bilge-pump DIY equivalents)
4x Electronic Speed Controllers (ESCs)
POWER
3S/4S LiPo battery
Power Distribution Board (PDB)
Inline fuse + master kill switch
STRUCTURE
Acrylic pressure tube + dome (main hull)
1/2" PVC / 3D-printed frame
O-rings, cable penetrators, marine epoxy
TETHER & SURFACE
20–50 m Cat5e/Cat6 tether cable
Control laptop
Joystick / controller box (Arduino-based or USB)

## Slide 10
10
Power System
How energy is supplied, regulated, and protected across the drone
LiPo Battery
(3S / 4S)
Fuse & Kill
Switch
Power Distribution
Board (PDB)
5V Regulated Rail
→ MCU, IMU, Depth & Leak
Sensors, Camera
11.1V / 14.8V Motor Rail
→ ESCs → Brushless
Thrusters
SUBMERSIBLE POWER (INSIDE THE HULL)
A single 3S/4S LiPo battery sits inside the sealed hull, kept low in the frame for stability. Power passes through an inline fuse and a manual kill switch before reaching the PDB, which regulates and splits the supply into a 5V logic rail for the microcontroller and sensors, and a higher-voltage motor rail feeding the ESCs and thrusters directly.
SURFACE-SIDE POWER
The control laptop runs on its own battery or a wall adapter; the joystick / surface controller box is powered separately via USB or its own battery pack — fully decoupled from the drone's onboard power so a surface fault can never affect the submersible unit.

## Slide 11
11
Software Components & Technologies
The firmware, protocols, and tools that bring the hardware to life
EMBEDDED FIRMWARE
C / C++ (Arduino IDE or PlatformIO)
Runs on the ESP32 / Arduino Mega
Sensor drivers for MPU6050 & MS5837
CONTROL ALGORITHM
PID stabilisation loop for depth & orientation hold
PWM signal generation for ESCs
Leak-triggered emergency ascent routine
COMMUNICATION PROTOCOL
Serial data over RS-485 (MAX485)
Lightweight custom packet framing
Command + telemetry channels over one tether
SURFACE CONTROL SOFTWARE
Python (Tkinter / PyQt) desktop GUI
Live video handling via OpenCV
Real-time telemetry dashboard (depth, battery, leak)
DESIGN & DEV TOOLS
Fritzing / KiCad for circuit design
Fusion 360 for hull & frame modelling
Git & GitHub for version control
TESTING & CALIBRATION
Sensor calibration scripts (IMU offset, depth zero)
Bench + pool test logging
Serial monitor / logic analyser for debugging

## Slide 12
12
Detailed Budget
Estimated cost breakdown (LKR)
Component | Qty | Unit Price (LKR) | Total (LKR)
ESP32 / Arduino Mega | 1 | 3,500 | 3,500
Waterproof brushless thrusters | 4 | 6,500 | 26,000
Electronic Speed Controllers (ESC) | 4 | 2,200 | 8,800
MPU6050 IMU sensor | 1 | 850 | 850
MS5837 depth / pressure sensor | 1 | 12,500 | 12,500
FPV / USB camera module | 1 | 4,500 | 4,500
LiPo battery (3S/4S) | 1 | 6,800 | 6,800
Power Distribution Board | 1 | 1,200 | 1,200
RS-485 (MAX485) modules | 2 | 450 | 900
Cat5e/Cat6 tether cable (30 m) | 1 | 4,500 | 4,500
Acrylic hull tube & dome | 1 | 8,000 | 8,000
PVC frame & 3D-printed brackets | 1 set | 5,000 | 5,000
O-rings, epoxy, cable glands | 1 set | 2,500 | 2,500
Fuses, kill switch & wiring | 1 set | 1,500 | 1,500
Joystick / controller box | 1 | 3,200 | 3,200
Contingency (~10%) | — | — | 8,000
TOTAL BUDGET
LKR 97,750
Approx. cost for one full prototype build
COST NOTES
• Prices are indicative market estimates and may vary by supplier.
• Thrusters can be substituted with DIY bilge-pump conversions to reduce cost.
• Contingency covers shipping, rework, and spares.

## Slide 13
13
Project Timeline
10-month development plan
M1
M2
M3
M4
M5
M6
M7
M8
M9
M10
Research & Requirements
System Design & Procurement
Hull Fabrication & Waterproofing
Hardware Integration (power, propulsion, sensors)
Firmware & Stabilisation (PID)
Communication & Surface GUI
Testing, Calibration & Pool Trials
Documentation & Final Presentation
Testing and documentation phases overlap deliberately with development to surface integration issues early.

## Slide 14
14
Work Distribution
Each member owns a role, at least one sensor, and a set of hardware modules
Member | Index No. | Primary Role | Hardware Modules Owned | Sensor Owned
CHAMIDYA J.A.S | 254037B | Mechanical Design & Waterproofing | Hull tube, frame, buoyancy/ballast, cable penetrators | Leak Detection Sensor
DE SILVA P.S.S | 254048J | Propulsion & Power Electronics | LiPo battery, PDB, ESCs, thrusters, fuse & kill switch | Battery Voltage/Current Sensor (INA219)
OMESH N.A.N | 255078H | Embedded Coding & Stabilisation | Microcontroller (ESP32/Arduino Mega), firmware, PID loop | IMU (MPU6050)
KALANSOORIYA O.K | 254101R | Communication & Video (Tether) | RS-485 modules, tether cable, strain relief | Camera (FPV/USB video sensor)
GOONATILLAKA W.A.D.S.S | 255027D | Surface Station & UI | Joystick controller, surface Arduino/laptop GUI | Depth/Pressure Sensor (MS5837) — calibration & live readout
Every member is directly responsible for at least one onboard sensor and its integration with the IoT/hardware stack.

## Slide 15
15
References
Sources consulted during research and design
1.
Science Buddies. (n.d.). Build an underwater robot (ROV). Science Buddies. https://www.sciencebuddies.org
2.
Blue Robotics. (n.d.). T200 thruster documentation. Blue Robotics. https://bluerobotics.com
3.
Blue Robotics. (n.d.). MS5837 pressure/depth sensor datasheet. Blue Robotics. https://bluerobotics.com
4.
Arduino. (n.d.). Choosing a microcontroller for robotics projects. Arduino Blog. https://blog.arduino.cc
5.
Zbotic. (n.d.). DIY underwater ROV component guide. Zbotic. https://zbotic.in
6.
Instructables. (n.d.). Building a surface control station for ROVs. Instructables. https://www.instructables.com
7.
Maxim Integrated / Analog Devices. (n.d.). MAX485 RS-485 transceiver datasheet.
8.
InvenSense / TDK. (n.d.). MPU6050 six-axis IMU datasheet.

## Slide 16
Thank You
Questions & Discussion
AquaScout — B25 FIT Level 01 Project